## Slide 1: RFID Technology Implementation at Style Textile
Efficiency, Accuracy & Real-Time Tracking in Production

## Slide 2: Why RFID in Style Textile?
Bundles can get lost or misrouted in stitching
Hard to track bundle locations in real time
Delay in production due to misplacement = lost time + money
Manual slips/tapes can fall off or get misplaced
Workers' wages can be calculated easily per parts

## Slide 3: Time Lost During Daily Production
Bundle Misplacement – 60 mins
Manual Bundle Sorting – 30 mins
Production Delays – 30 mins
Data Entry Errors – 20 mins
WIP Tracking & Reporting – 60 mins
Total = 200 mins (3.33 hours approx.)

## Slide 4: Current Flow vs RFID Process
Cutting – RFID tag with encoded info instead of slips
WIP Transfer – RFID logs dispatch automatically
Stitching – RFID detects arrival at each station
Progress Tracking – System tracks stage automatically
Issue Resolution – System flags last known bundle location

## Slide 5: RFID Equipment Required
RFID Tags – Reusable UHF tags (1 per bundle)
RFID Readers – Fixed UHF readers at 9 locations
Antennas – Directional patch antennas (6–9 dBi)
Cables & Power – Coaxial cables, PoE adapters
Database / ERP Integration – Real-time dashboards
Computing & Networking – PC/server, switches, Wi-Fi APs

## Slide 6: Reader Placement at Workstations
Cutting → WIP handoff – 1
WIP → Stitching entry – 1
Small Parts – 1
Back Sections (L3 & L4) – 1
Fashion Hall – 1
Back Section (L1 & L2) – 1
Front Section (L1 & L2) – 1
Assembly-I (L1 & L2) – 1
Assembly-II (L1 & L2) – 1
Total = 9 Readers

## Slide 7: Daily Bundle Estimation at Style Textile
1 lay = 17 fabric layers = 17 jeans (mixed sizes)
Each lay produces 51 bundles
Daily jeans output = 22,000
Total bundles/day = 22,000 / 51 ≈ 431
Round off to 450 RFID tags/shift (buffer included)

## Slide 8: Cost Analysis of RFID Implementation
RFID Tags (450) – ₨ 189,900
RFID Readers (9) – ₨ 759,510
Software & Integration – ₨ 281,300
Installation & Training – ₨ 140,650
Total Cost – ₨ 1,371,360

## Slide 9: Time Saved with RFID System
Bundle Misplacement – Resolved via auto-location (60 min)
Manual Sorting – Instant scan (30 min)
Production Delay – Real-time updates (30 min)
Data Entry Errors – Digital data (20 min)
WIP Tracking – Automated reports (40 min)
Total Saved = 180 min (3 hours approx.)

## Slide 10: Throughput Comparison
Without RFID – 413 bundles/day, 41 bundles/hour
With RFID – Save 3 hours = 123 additional bundles
Total with RFID = 536 bundles/day
New Throughput = 54 bundles/hour